| SCHEDULE OF QUANTITIES |
| --- |
| Name of work: Construction of Playground & Parking in Govt. ITI GarhJamula. Distt. Kangra (HP). (SH: Survey of Plot) |
| SI.No. | Description of Item | Quantity | Unit | Rate (both in words & figures) Rs. | Amount (Rs.) |
| 1 | Conducting topographical survey with electronic theodolite or any suitable method showing position of boundary lines, bench mark, contour lines at 1.00 m interval, highest flood level , adjoining features such as near by buildings, electric poles & lines , telephone poles, trees, river/nalah, roads, pucca paths, water supply and sewer lines, manholes etc. (as detailed in the scope of work enclosed as per Annexure "Y" ) and providing soft copy as well as 6 (Six) nos. prints of Surveyed Site Plan complete in all respect and as per the directions of Engineer-in-charge. | 12000.00 | SQM |  |  |
|  | Total |  |  |

( Notes:- Quoted rates should be inclusive of GST)

Executive Engineer (C)

BSNL Civil Division,

Dharamshala (HP).

ANNEXURE ‘Y’

SCOPE OF WORK FOR TOPOGRAPHICAL SURVEY, COLLECTION OF FIELD DATA AND REPORT SUBMISSION

The Scope of work is detailed as under:-

- Carrying out topographical survey.

- Spot levelling of total area of land/plot by taking spot levels at 2 m centre to centre grid and contour intervals at 1.0 m, showing clear boundary details with triangulation distances. The spot levels should be taken and the contour lines drawn upto atleast 5.00 m outside the boundary line on all sides.

- To locate on the survey plan in A1/A0 sheet to the scale of 1:200 with all permanent & temporary structures along with existing storm, sewer & water line, power (HT & LT) & telecommunication lines/poles, trees of various girths, roads, water supply, sewer, drainage line and also any other important features etc. adjacent and within the total area of plot, if any. The position of temporary bench mark should also be properly marked and shown in the survey sheet.

- Direction of North should also be marked on the plan.

- Details about Sewer and storm water drain / nallah passing through/near the complex should be marked on survey plan.

- Location of the roads such as Gagal to Bus stand Dharamshala , approach roads from main road to site and other paths near the site indicating its layout [Index Plan] with reference to site.(These detailed shall not be measured in plot area for  payments)

- Details of Municipal / Public sewer line / Manholes near the plot should also be shown.

- Details of proposed approach road connecting main road to project site to be supplied showing the alignment of the road.

- Detail of the existing boundary wall/hedges, temporary and permanent structures, if any, inside the site including the following shall be collected and supplied:-

    - Cross section of the boundary wall.

    - Part elevations and cross-section of the buildings also showing foundation.

    - Length, width, height, area and no of stories of each building including details of materials used in construction.

    - Location of existing trees (along with height and girth of the trees) and other permanent / temporary structures.

    - Electric overhead lines (LT/HT), telephone lines.

- All survey, grid levels shall be done by Total Station or any other software and contour plan shall be prepared on computer through digitisation process and the soft copy in PDF format and/or Auto CAD format shall be provided for the same.

- On completion of all fieldwork, collection of pertinent field data and preparation of drawings the agency shall submit a formal draft report containing all the information/field observations and drawings, in triplicate for review of the Engineer-in- Charge . Thereafter the agency shall visit to Engineer-in-charge’s office for detail discussions on his comments if any. After discussion the agency shall incorporate the agreed modifications in the draft report at their own cost and submit 6 sets of drawings (the drawings shall bear the logo of BSNL and the format of the same can be obtained from Engineer-in-charge’s office) along with a set of reproducible drawings and related CD.

- Plot has to be cleared of all vegetation including shrubs, bushes, etc. whatsoever before start of the work and all removed vegetation to be thrown as per BSNL directives.

# Executive Engineer (C)

# BSNL Civil Division,

# Dharamshala (HP).