| SCHEDULE OF QUANTITIES |
| --- |
| Name of work: Minor Repair of some structural members of old Telephone Exchange Building at Chamba (HP) |
| SI. No. | Description of Item | Quantity | Rate (both in words & figures) Rs. | Unit | Amount (Rs.) |
|  | SH: Finishing |  |  |  |
| 1 | 15 mm cement plaster on rough side of single or half brick wall of mix : |  |  |  |  |  |
| a) | 1:4 (1 cement: 4 coarse sand) | 100.00 | Sqm |  | One Square Metre |  |
| 2 | Finishing walls with Premium Acrylic Smooth exterior paint with Silicone additives of required shade |  |  |  |  |  |
| a) | New work (Two or more coats applied @ 1.43 ltr/ 10 sqm. over and including priming coat of exterior primer applied @ 2.20 kg/10 sqm). | 100.00 | Sqm |  | One Square Metre |  |
|  | SH: Repairs to buildings |  |  |  |  |  |
| 1 | Providing and fixing double scaffolding system (cup lock type) on the exterior side, up to seven story height made with 40mm dia. M.S. tube 1.5m centre to centre horizontal & vertical tubes joining with cup & lock system with M.S. tubes, M.S. tube challies, M.S. clamps and M.S. staircase system in the scaffolding for working platform etc. and maintaining it in a serviceable condition for the required duration as approved and removing it there after. The scaffolding system shall be stiffened with bracings, runners, connection with the building etc. wherever required for inspection of work at required locations with essential safety features for the workmen etc. complete as per directions and approval of Engineer-in-charge .The elevational area of the scaffolding shall be measured for payment purpose. The payment will be made once irrespective of duration of scaffolding. | 100.00 | Sqm |  | One Square Metre |  |
|  | SH: Dismantling & Demolishing |  |  |  |  |  |
| 1 | Dismantling old plaster or skirting raking out joints and cleaning the surface for plaster including disposal of rubbish to the dumping ground within 50 metres lead. | 80.00 | Sqm |  | One Square Metre |  |
| 2 | Disposal of building rubbish / malba / similar unserviceable, dismantled or waste materials by mechanical means, including loading, transporting, unloading to approved municipal dumping ground or as approved by Engineer-in-charge, beyond 50 m initial lead, for all leads including all lifts involved. | 2.00 | Cum |  | One Cubic Metre |  |

Executive Engineer (C)

BSNL Civil Division,

Dharamshala (HP).