| Office of the Executive Engineer (C) BSNL Civil Division, Block No-5, 4th Floor, Phase-III, Sector-6, Kangnadhar, New Shimla-171009. Telephone: 0177 2673088 Fax: 2673828 |  |
| --- | --- |

Name of work:-“Provision of 2 Nos. G.I Pipes / Poles for improvement of Mobile Signal in the residence of Hon’ble Chief Justice of HP High Court at Chaura Maidan, Shimla (HP).”

| SCHEDULE OF QUANTITIES |
| --- |
| I.No. | Description of Item | Quantity | Rate (Rs) | Unit | Amount (Rs) |
|  | Sub–Head : Earth Work. |  |  |  |  |  |
| 1 | Earth work in excavation by mechanical means (Hydraulic excavator) / manual means in foundation trenches or drains (not exceeding 1.5 m in width or 10 sqm on plan) including dressing of sides and ramming of bottoms, lift up to 1.5 m, including getting out the excavated soil and disposal of surplus excavated soil as directed, within a lead of 50 m. |  |  |  |  |  |
| a) | All kinds of soil. | 1.50 | Cum |  | One Cubic Metre |  |
|  | Sub-Head : Concrete Work |  |  |  |  |  |
| 2 | Providing and laying in position cement concrete of specified grade excluding the cost of centering and shuttering - All work up to plinth level : |  |  |  |  |  |
| a) | 1:2:4 (1 cement : 2 coarse sand(zone-III) : 4 graded stone aggregate 20 mm nominal size) | 0.35 | Cum |  | One Cubic Metre |  |
| 3 | Centering and shuttering including strutting, propping etc. and removal of form work for : |  |  |  |  |  |
| a) | Retaining walls, return walls, walls (any thickness) including attached pilasters, buttresses, plinth and string courses fillets, kerbs and steps etc.. | 1.50 | Sqm |  | One Square Metre |  |
| 4 | Providing and laying in position cement concrete 1:3:6 (1 cement: 3 coarse sand: 6 graded stone aggregate 40mm nominal size) with 40% plums/stone boulders of specified grade and size and curing complete excluding the cost of centering and shuttering in retaining walls & breast walls. The size of plums shall usually be 150mm to 300mm as per the directions of the Engineer-in-charge. | 2.00 | Cum |  | One Cubic Metre |  |
|  | Sub-Head : Steel Work |  |  |  |  |  |
| 5 | Steel work welded in built up sections/ framed work, including cutting, hoisting, fixing in position and applying a priming coat of approved steel primer using structural steel etc. as required. |  |  |  |  |  |
| a) | In gratings, frames, guard bar, ladder, railings, brackets, gates and similar works. | 105.00 | Kg |  | One Kilogram |  |
| 6 | Providing and fixing antenna poles of approved size by welding etc. to steel ladder, support etc. including applying priming coat of approved steel primer. |  |  |  |  |  |
| a) | G.I. pipes | 145.00 | Kg |  | One Kilogram |  |
|  | Sub-Head : Finishing |  |  |  |  |  |
| 7 | Painting with synthetic enamel paint of approved brand and manufacture to give an even shade : |  |  |  |  |  |
| a) | Two or more coats on new work. | 10.00 | Sqm |  | One Square Metre | 0 |
|  | Total Rs- |  |

Executive Engineer (C)

BSNL, Civil Division,

Shimla (HP).