O/o Executive Engineer (C)                                                          (A Govt. of India Enterprise)

BSNL Civil Division

Dharamshala-176215[H.P]Tel: 01892-226072 Fax: 01892-226199

Email: eebsnldma123@gmail.com

----------------------------------------------------------------------------------------------------------------

No:-03/EE/BSNL/CD/DMA/2024-2025                                                     Dated:- 26.04.2024

S C H E D U L E O F Q U A N T I T Y

Name of work :-

Repair and maintenance of GM Office at Chilgari, Dharamshala, Distt. Kangra (HP).

| S no | Description of items | Quantity | Unit | Rate (both in words & figures) Rs. | Amount (Rs.) |
| --- | --- | --- | --- | --- | --- |
|  | Sub-Head : Dismantling and Demolishing |  |  |  |  |  |
| 1 | Dismantling tile work in floors and roofs laid in cement mortar including stacking material within 50 metres lead. |  |  |  |  |  |
| a) | For thickness of tiles 10 mm to 25 mm | 6.00 | Sqm | One Square Metre |  |  |
|  | Sub-Head : Cladding Work |  |  |  |  |  |
| 2 | Providing and fixing Ist quality ceramic glazed wall tiles conforming to IS: 15622 (thickness to be specified by the manufacturer), of approved make, in all colours, shades except burgundy, bottle green, black of any size as approved by Engineer-in-Charge, in skirting, risers of steps and dados, over 12 mm thick bed of cement mortar 1:3 (1 cement : 3 coarse sand) and jointing with grey cement slurry @ 3.3kg per sqm, including pointing in white cement mixed with pigment of matching shade complete. | 1.00 | Sqm | One Square Metre |  |  |
|  | Sub-Head : Flooring |  |  |  |  |  |
| 3 | Providing and laying Ceramic glazed floor tiles of size 300x300 mm(thickness to be specified by the manufacturer) of 1st quality conforming to IS : 15622 of approved make in colours such as White, Ivory, Grey, Fume Red Brown, laid on 20 mm thick cement mortar 1:4 (1 Cement :4 Coarse sand), jointing with grey cement slurry @ 3.3kg/sqm including pointing the joints with white cement and matching pigment etc. complete. | 5.00 | Sqm | One Square Metre |  |  |
|  | Sub-Head : Finishing |  |  |  |  |  |
| 4 | Providing and applying white cement based putty of average thickness 1 mm, of approved brand and manufacturer, over the plastered wall surface to prepare the surface even and smooth complete. | 7.00 | Sqm | One Square Metre |  |  |
| 5 | Wall painting with acrylic emulsion paint, having VOC (Volatile Organic Compound ) content less than 50 grams/ litre, of approved brand and manufacture, including applying additional coats wherever required, to achieve even shade and colour. |  |  |  |  |  |
| a) | Two coats. | 128.00 | Sqm | One Square Metre |  |  |
| 6 | Removing white or colour wash by scrapping and sand papering and preparing the surface smooth including necessary repairs to scratches etc. complete | 7.00 | Sqm | One Square Metre |  |  |
| 7 | Painting with synthetic enamel paint of approved brand and manufacture of required colour to give an even shade : |  |  |  |  |  |
| a) | One or more coats on old work. | 38.00 | Sqm | One Square Metre |  |  |
|  | Sub-Head : Sanitary Installations |  |  |  |  |  |
| 8 | Providing and fixing white vitreous china pedestal type water closet (European type W.C. pan) with seat and lid, 10 litre low level white P.V.C. flushing cistern, including flush pipe, with manually controlled device (handle lever), conforming to IS : 7231, with all fittings and fixtures complete, including cutting and making good the walls and floors wherever required : |  |  |  |  |  |
| (a) | W.C. pan with ISI marked white solid plastic seat and lid | 1.00 | Nos. | Each |  |  |
| 9 | Providing and fixing white vitreous china flat back or wall corner type lipped front urinal basin of 430x260x350 mm and 340x410x265 mm sizes respectively with automatic flushing cistern with standard flush pipe and C.P. brass spreaders with brass unions and G.I clamps complete, including painting of fittings and brackets, cutting and making good the walls and floors wherever required : |  |  |  |  |  |
| a) | One urinal basin with 5 litre white P.V.C. automatic flushing cistern | 1.00 | Nos. | Each |  |  |
| 10 | Providing and fixing P.V.C. waste pipe for sink or wash basin including P.V.C. waste fittings complete. |  |  |  |  |  |
| a) | Flexible pipe |  |  |  |  |  |
| i) | 32 mm dia | 2.00 | Nos. | Each |  |  |
| 11 | P/F high pressure upvc SELFITsingle socket waste and ventilating pipes conforming to IS 13592 Type B including jointing with adhesive leaving 10mm gap for thermal expansion |  |  |  |  |  |
| a) | 90 mm diameter | 2.00 | Mtr | Metre |  |  |
| b) | 110 mm diameter | 1.00 | Mtr | Metre |  |  |
| 12 | P/F upvc moulded SELFIT fittings for waste and ventilating pipes including jointing with adhesive leaving 10mm gap for thermal expansion. |  |  |  |  |  |
| a) | Door Bend 87.5 degree: 110 mm bend. | 1.00 | Nos. | Each |  |  |
| b) | Socket: 110 mm . | 1.00 | Nos. | Each |  |  |
| c) | Offset Bend: 90 mm . | 2.00 | Nos. | Each |  |  |
| d) | Single tee with door: 110 x 110 x 110 mm. | 1.00 | Nos. | Each |  |  |
| e) | P-Trap 125x110mm | 1.00 | Nos. | Each |  |  |
| 13 | P/F upvc moulded SELFIT fittings for waste and ventilating pipes including jointing with adhesive leaving 10mm gap for thermal expansion - Floor Trap 110x90mm. | 1.00 | Nos. | Each |  |  |
| 14 | Providing and fixing hinged stainless steel jali (grating) with or without hole for waste pipe for floor/Nahni trap. | 1.00 | Nos. | Each |  |  |
|  | Sub-Head : Water Supply |  |  |  |  |  |
| 15 | Providing and fixing Chlorinated Polyvinyl Chloride (CPVC) pipes, having thermal stability for hot & cold water supply, including all CPVC plain & brass threaded fittings, i/c fixing the pipe with clamps at 1.00 m spacing. This includes jointing of pipes & fittings with one step CPVC solvent cement and the cost of cutting chases and making good the same including testing of joints complete as per direction of Engineer in Charge. Concealed work, including cutting chases and making good the walls. |  |  |  |  |  |
| a) | 20 mm nominal outer dia .Pipes. | 15.00 | Mtr | One Running Metre |  |  |
| 16 | Providing and fixing ball valve (brass) of approved quality, High or low pressure, with plastic floats complete : |  |  |  |  |  |
| a) | 20 mm nominal bore | 4.00 | Nos. | Each |  |  |
| 17 | Providing and fixing uplasticised PVC connection pipe with brass unions : |  |  |  |  |  |
| a) | 30 cm length |  |  |  |  |  |
| i) | 15 mm nominal bore | 6.00 | Nos. | Each |  |  |
| 18 | Providing and fixing C.P. brass bib cock of approved quality conforming to IS:8931: |  |  |  |  |  |
| a) | 15 mm nominal bore. | 2.00 | Nos. | Each |  |  |
| 19 | Providing and fixing C.P. brass angle valve for basin mixer and geyser points of approved quality conforming to IS:8931 : |  |  |  |  |  |
| a) | 15mm nominal bore | 6.00 | Nos. | Each |  |  |
| 20 | Providing and fixing PTMT extension nipple for water tank pipe, fittings of approved quality and colour. |  |  |  |  |  |
| a) | 20mm nominal bore. Weighing not less than 40 gms. | 4.00 | Nos. | Each |  |  |
| 21 | Providing and fixing Chlorinated Polyvinyl Chloride (CPVC) gate valve in Chlorinated Polyvinyl Chloride (CPVC) pipe etc. complete (New work) : |  |  |  |  |  |
| (a) | 20 mm nominal bore | 4.00 | Nos. | Each |  |  |
|  | Sub-Head : Miscellaneous |  |  |  |  |  |
| 22 | Providing and laying 1.50 mm thick polyvinyle chloride sheet in floor/skirting on a smooth base using rubber based adhesive (viz Dunlop S 758, Fevicol SR 505 or equivalent) including cleaning levelling and drying of base including rolling with light wooden roller weighing about 5 Kg, all compete as per specifications and per direction of the Engineer-in-charge. | 45.00 | sqm | One Square Metre |  |  |
| 23 | Credit for following old unserviceable materials:- |  |  |  |  |  |
| i ) | Stop cock /bib cock/ Mixer /Angle valve & alike. | 6.00 | Nos | each |  |  |
| ii) | PVC Cistern . | 1.00 | Nos | each |  |  |

( Note:- Quoted rates should be inclusive of  GST)

EXECUTIVE  ENGINEER (C),

BSNL CIVIL DIVISION ,

DHARAMSHALA.

Last corrected on 26/04/2024